## Slide 1: Counting Corals from the Air
Drone photogrammetry for reef monitoring · Department seminar · 12 March 2026 · Lena Fischer

## Slide 2: Agenda
Motivation
Study sites
Methods
Results
Limitations and next steps

## Slide 3: Motivation
Live coral cover on monitored reefs fell by a third since 2010
Diver transects cover < 1% of a reef and take weeks
Managers need yearly, reef-wide estimates
Notes: Start with the photo of the bleached patch from 2024; ask how many people have done a transect survey.

## Slide 4: Study sites
Six fringing reefs, 0.5–4 m deep at low tide
Paired diver transects at 40 permanent plots
Flights within two hours of low water, wind < 10 knots

## Slide 5: Methods
Consumer drone, 20 MP camera, 80% image overlap
Structure-from-motion: orthomosaic at 6 mm per pixel
Segmentation network trained on 3,100 annotated tiles
  Classes: live coral, dead coral, algae, sand, rubble

## Slide 6: Results
Metric | Drone | Divers
Area surveyed per day (ha) | 14.2 | 0.3
Live coral cover (%) | 23.8 | 25.1
Agreement (Lin's CCC) | 0.91 | -
Notes: Emphasise that the bias is small and constant, so trends are reliable.

## Slide 7: Limitations
Glint and turbidity remove 8–15% of each mosaic
Cannot see under overhangs or identify species
Requires calm, clear conditions

## Slide 8: Next steps and acknowledgements
Multispectral camera to separate bleached from healthy coral
Open dataset release later this year
Thanks to the field team and the Marine Parks Authority (fictional)